## Slide 1: Lecture 1: Images and image filtering
Computer Vision
Hybrid Images, Oliva et al., http://cvcl.mit.edu/hybridimage.htm

## Slide 2: Reading
Szeliski, Chapter 3.1-3.2

## Slide 3: What is an image?

## Slide 4: What is an image?
Digital Camera
The Eye
Source: A. Efros
We’ll focus on these in this class
(More on this process later)

## Slide 5: What is an image?
A grid (matrix) of intensity values
(common to use one byte per value: 0 = black, 255 = white)
=
255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255
255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255
255 | 255 | 255 | 20 | 0 | 255 | 255 | 255 | 255 | 255 | 255 | 255
255 | 255 | 255 | 75 | 75 | 75 | 255 | 255 | 255 | 255 | 255 | 255
255 | 255 | 75 | 95 | 95 | 75 | 255 | 255 | 255 | 255 | 255 | 255
255 | 255 | 96 | 127 | 145 | 175 | 255 | 255 | 255 | 255 | 255 | 255
255 | 255 | 127 | 145 | 175 | 175 | 175 | 255 | 255 | 255 | 255 | 255
255 | 255 | 127 | 145 | 200 | 200 | 175 | 175 | 95 | 255 | 255 | 255
255 | 255 | 127 | 145 | 200 | 200 | 175 | 175 | 95 | 47 | 255 | 255
255 | 255 | 127 | 145 | 145 | 175 | 127 | 127 | 95 | 47 | 255 | 255
255 | 255 | 74 | 127 | 127 | 127 | 95 | 95 | 95 | 47 | 255 | 255
255 | 255 | 255 | 74 | 74 | 74 | 74 | 74 | 74 | 255 | 255 | 255
255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255
255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255

## Slide 6: What is an image?
We can think of a (grayscale) image as a function, f, from R2 to R:
  f (x,y) gives the intensity at position (x,y)
  A digital image is a discrete (sampled, quantized) version of this function
x
y
f (x, y)
snoop
3D view

## Slide 7: Image transformations
As with any function, we can apply operators to an image
Today we’ll talk about a special kind of operator, convolution (linear filtering)
  g (x,y) = f (x,y) + 20
  g (x,y) = f (-x,y)

## Slide 8: Filters
Filtering
  Form a new image whose pixels are a combination of the original pixels
Why?
  To get useful information from images
    E.g., extract edges or contours (to understand shape)
  To enhance the image
    E.g., to remove noise
    E.g., to sharpen and “enhance image” a la CSI

## Slide 9: Canonical Image Processing problems
Image Restoration
  denoising
  deblurring
Image Compression
  JPEG, JPEG2000, MPEG..
Computing Field Properties
  optical flow
  disparity
Locating Structural Features
  corners
  edges

## Slide 10: Question: Noise reduction
Given a camera and a still scene, how can you reduce noise?
Take lots of images and average them!
What’s the next best thing?
Source: S. Seitz
Notes: Answer: take lots of images, average them

## Slide 11: Image filtering
Modify the pixels in an image based on some function of a local neighborhood of each pixel
5
1
4
1
7
1
5
3
10
Local image data
7
Modified image data
Some function
Source: L. Zhang

## Slide 12: Linear filtering
One simple version of filtering: linear filtering (cross-correlation, convolution)
  Replace each pixel by a linear combination (a weighted sum) of its neighbors
The prescription for the linear combination is called the “kernel” (or “mask”, “filter”)
0.5
0.5
0
0
1
0
0
0
0
kernel
8
Modified image data
Source: L. Zhang
Local image data
6
1
4
1
8
1
5
3
10

## Slide 13: Cross-correlation
This is called a cross-correlation operation:
Let be the image, be the kernel (of size 2k+1 x 2k+1), and be the output image
Can think of as a “dot product” between local neighborhood and kernel for each pixel

## Slide 14: Convolution
Same as cross-correlation, except that the kernel is “flipped” (horizontally and vertically)
Convolution is commutative and associative
This is called a convolution operation:

## Slide 15: 1D Demo

## Slide 16: Convolution
Adapted from F. Durand

## Slide 17: Mean filtering
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 1 | 1
1 | 1 | 1
1 | 1 | 1
*
=
 | 0 | 10 | 20 | 30 | 30 | 30 | 20 | 10 | 
 | 0 | 20 | 40 | 60 | 60 | 60 | 40 | 20 | 
 | 0 | 30 | 60 | 90 | 90 | 90 | 60 | 30 | 
 | 0 | 30 | 50 | 80 | 80 | 90 | 60 | 30 | 
 | 0 | 30 | 50 | 80 | 80 | 90 | 60 | 30 | 
 | 0 | 20 | 30 | 50 | 50 | 60 | 40 | 20 | 
 | 10 | 20 | 30 | 30 | 30 | 30 | 20 | 10 | 
 | 10 | 10 | 10 | 0 | 0 | 0 | 0 | 0 | 

## Slide 18: Mean filtering/Moving average

## Slide 19: Mean filtering/Moving average

## Slide 20: Mean filtering/Moving average

## Slide 21: Mean filtering/Moving average

## Slide 22: Mean filtering/Moving average

## Slide 23: Mean filtering/Moving average

## Slide 24: Example filters
Original
1
1
1
1
1
1
1
1
1
Blur (with a
box filter)
Source: D. Lowe

## Slide 25: Linear filters: examples
0
0
0
0
1
0
0
0
0
Original
Identical image
Source: D. Lowe
*
=

## Slide 26: Linear filters: examples
0
0
0
0
0
1
0
0
0
Original
Shifted left
By 1 pixel
Source: D. Lowe
*
=

## Slide 27: Linear filters: examples
Original
1
1
1
1
1
1
1
1
1
Blur (with a mean filter)
Source: D. Lowe
*
=

## Slide 28: Linear filters: examples
Original
1
1
1
1
1
1
1
1
1
0
0
0
0
2
0
0
0
0
-
Sharpening filter (accentuates edges)
Source: D. Lowe
=
*

## Slide 29: Sharpening
Source: D. Lowe

## Slide 30: Smoothing with box filter revisited
Source: D. Forsyth
Notes: I always walk through the argument on the left rather carefully; it gives some insight into the
significance of impulse responses or point spread functions.

## Slide 31: Gaussian Kernel
Constant factor at front makes volume sum to 1 (can be ignored, as we should re-normalize weights to sum to 1 in any case)
0.003 0.013 0.022 0.013 0.003
0.013 0.059 0.097 0.059 0.013
0.022 0.097 0.159 0.097 0.022
0.013 0.059 0.097 0.059 0.013
0.003 0.013 0.022 0.013 0.003
5 x 5,  = 1
Source: C. Rasmussen

## Slide 32: Gaussian Kernel
Source: C. Rasmussen

## Slide 33: Gaussian filters
= 30 pixels
= 1 pixel
= 5 pixels
= 10 pixels

## Slide 34: Mean vs. Gaussian filtering

## Slide 35: Gaussian filter
Removes “high-frequency” components from the image (low-pass filter)
Convolution with self is another Gaussian
  Convolving twice with Gaussian kernel of width = convolving once with kernel of width
Source: K. Grauman
*
=
Notes: Linear vs. quadratic in mask size

## Slide 36: Sharpening revisited
What does blurring take away?
original
smoothed (5x5)
–
detail
=
sharpened
=
Let’s add it back:
original
detail
+ α
Source: S. Lazebnik
(This “detail extraction” operation is also called a high-pass filter)

## Slide 37: Sharpen filter
Gaussian
scaled impulse
Laplacian of Gaussian
image
blurred image
unit impulse (identity)
Notes: f + a(f - f * g) = (1+a)f-af*g = f*((1+a)e-g)

## Slide 38: Sharpen filter
unfiltered
filtered

## Slide 39: “Optical” Convolution
Source: http://lullaby.homepage.dk/diy-camera/bokeh.html
Bokeh: Blur in out-of-focus regions of an image.
Camera shake
*
=
Source: Fergus, et al. “Removing Camera Shake from a Single Photograph”, SIGGRAPH 2006

## Slide 40: Filters: Thresholding

## Slide 41: Linear filters
Is thresholding a linear filter?

## Slide 42: Questions?
Spatial-Invariant VS Spatial-Aware
Local VS Global